## Slide 2
1,1
0,0
nREalx,nRealy
nRealx+1,nRealy+1
Linear System:
A*phi = b
Size of system: N x N
Where N = (nRealx+2)(nRealy+2)
Silver Nodes are of Equal Standing with Red Nodes
Dirichlet BCs are Applied to all Silver Nodes
-- Some are due to mesh on adjacent processor
-- Some are actual BCs.
-- The Silver Nodes can be outside the problem Domain
Dirichlet BCs can also be applied to Red Nodes on Boundary of Domain

## Slide 3
1,1
0,0
nRealx,nRealy
Let the lines shown denote “communication” between nodes in the linear system
A phi = b
When a Dirichlet BC is applied to node “k”, the kth row of A has a 1 on the diagonal and the rest of the columns on that row are zero. Thus, on row k, the k node does not communicate with other nodes. However, other adjacent nodes may communicate with node k on their row, though, if they do not have a Dirichlet BC.
Here we show the resulting communication between nodes when the Dirichlet BCs on the silver nodes are taken into account. More lines would disappear when the physical BCs are applied as well.
The key point is this: The corner silver nodes do not communicate with anything.
nRealx+1,nRealy+1

## Slide 4
Problem Domain, Divided into Four Processors
Bottom-Left (Red) Processor’s Grid
Physical BCs
BCs from Other Grids